## Slide 1: VSG2 Basic Information
  VSG2 is a Twyman-Green interferometer with the camera focused on the DM, which serves as the system pupil.
    It will be updated to include Zernike Wavefront Sensor (ZWFS)
  Source: frequency stabled He-Ne laser feed into SM fiber
    Baffle to block excessive light outside the L1
  Collimate lens (L1): Achromatic Doublet Lens, Visible, D=76.2 mm, 750 mm EFL, 430-700 nm.
    https://www.newport.com/p/PAC097AR.14
  Beam splitter:
  Focusing lens (L2): Achromatic Doublet Lens, Visible, D=76.2 mm, 250 mm EFL, 430-700 nm
    https://www.newport.com/p/PAC095AR.14
    Total length from DM to focusing lens ~1175 mm
  Camera: Andor NEO sCMOS
    2160x2560 array of 6.5 µm pixels
    Camera is focused to DM surface
    Distance from focusing lens to camera is ~317 mm
VSG2 Optical Layout
~1175 mm
~317 mm
DM
Ref Mirr & PZT Stage
Camera
Fold 1
Fold 2
BS
Baffle
L2
L1
ND
Source

## Slide 2: VSG2 In Picture
DM
Ref Mirr & PZT Stage
Camera
Fold 1
Fold 2
BS
Baffle
L2
L1
ND
VSG2 Test Article: Deformable Mirror (DM)
VSG2 Chamber
VSG2 Bench Inside Chamber
VSG2 Rack