## Slide 1
A 6 m unobscured coronagraph, end to end — with the loop closed
An optical design, its segmentation, its instrument with deformable mirrors and metrology, its error budget and its corrected drift — one model, one train
Conventions, stated once. Wavefront error is RMS at 500 nm at the exit pupil of the configuration being quoted — the telescope's own for the telescope-only slides, the coronagraph's once the instrument is attached (and every model-vs-engine check is evaluated at the surface its sensitivity model was harvested at). Contrast is the dark-zone mean over 3–15 λ/D, normalised to the bare on-axis peak of the same train; static scoring at a 1024 grid, the drift series at 512 (its control operator's grid). The diffraction limit is 0.071 waves RMS. Packaging is a deployed, diameter-only fit in an 8 m launch shroud.
Built with MACOS / mmacos. Every number on these slides is parsed from the committed stage reports; no figure was redrawn for the deck.
DRAFT (2026-08-27): the coronagraph-family slides (families / floors / Lyot trade) await Dave's review of the CF1c-CF3a numbers.

## Slide 2
The telescope
0.0473 waves RMS across the field — diffraction-limited at 500 nm
• The design. A 6 m unobscured three-mirror telescope: three base spheres placed for packaging, fold tilts doing the unobscuration, all correction carried by Zernike surface departures. Field ±0.35 arcmin.
• The wavefront. 0.0473 waves RMS worst case over the field, against a 0.071-wave diffraction limit.
• The packaging. 7.450 m diameter against the 8 m shroud; 1185/1185 rays survive a standalone reload of the saved prescription.
• The one miss. Focal ratio f/25.39 against a requested f/12–20; not a tuning failure — see the backup.
The three-mirror train: light enters from the left, folds back to the secondary, returns past the primary to the tertiary and the focus.
Wavefront error over the design field. Worst corner 0.0473 waves.

## Slide 3
The segmented primary
19 segments, and a poke that stays where it is put
• The segmentation. 19 hexagonal segments, 1.2 m flat to flat, 25 mm gaps, each carrying the parent's solved figure and its own physical polygonal aperture.
• The apertures are real. 983 of 985 traced rays survive the declared polygons, and a standalone reload reproduces the count — the check that catches a wrongly-framed aperture.
• The check that matters. Displace one segment 10 nm along its normal: the wavefront responds 19.91 nm over the 52 rays on that segment and exactly zero over the other 930.
Traced footprints against the emitted aperture polygons. Colour is the segment a ray landed on; black is the declared glass.

## Slide 4
The instrument, in light order
Eight relay mirrors, two deformable mirrors, five mask and pupil stations, two cameras
• One train. From the segmented primary through the fold train to the collimated pupil, then the coronagraph leg — DMs, apodizer, occulter, Lyot, field stop, back-end pupil, detector — with a deployable pick-off feeding the imager. Spliced as 37 elements of one prescription; 983/985 rays, the telescope's own count.
Light order through both instruments, read from the prescriptions. Orange marks the deformable mirrors, purple the mask and pupil sites, dashed the focus stations.

## Slide 5
Two instruments, one shroud
A second camera still costs nothing in diameter
• The coronagraph leg carries the science train: 37 elements, chief ray through the diffraction model agreeing with the geometric one to 5e-16.
• The imager leg. A deployable pick-off just after the collimator feeds its own f/19 camera: 0.0042 waves RMS, Strehl 0.9993 — unchanged from the round-1 stage that built it, because the pick-off sits upstream of everything round 2 added.
• Both fit. 7.451 m against the 8 m shroud for either leg and for the union; the 6 m primary sets the envelope.
Both legs down the launch axis, inside the 8 m shroud circle.

## Slide 6
The back end on its bench
Eight relay mirrors and two DMs in a 5.1 × 0.6 m accordion
• The drawing is to scale, in the plane the folds live in: the collimator, the DM pocket, then the mask relay — each mask plane sitting between its focus and pupil mirrors.
• Near-normal folds (6°) keep each off-axis section gentle; folding every mirror to the same side ping-pongs the beam into a bench-sized pocket. The other choice fans the chain 120° and breaks the shroud — measured, in the backup.
• In the full train the back end is centimetre-class against the 6 m primary — the reason it gets its own drawing.
The back end in its fold plane, to scale. Orange: the DMs at the collimated pupil. Purple: apodizer, Lyot and back-end pupil sites. White: the occulter and field-stop foci.
The full train for scale: the 6 m segmented primary and the beam it feeds.

## Slide 7
The masks, as physical objects
An occulter 2.8 λ/D across at a 500 nm focus is 27 µm of metal
• The occulter is an opaque disk of radius 2.8 λ/D at the intermediate focus — 27.3 µm physical radius at the measured 9.76 µm-per-λ/D focal scale, drawn from the same engine quantities the scoring chain uses.
• The apodizer is the clear-pupil prolate the coronagraph is scored with, shown as manufactured and as the light sees it — over the traced 19-segment pupil, gaps and all.
• Both figures are the scoring masks rebuilt from the scoring parameters, not illustrations.
The apodizer: the prolate transmission profile (left) and the same profile over the traced segmented pupil (right), mm at the 47 mm pupil.
The focal-plane occulter, transmission against λ/D; the physical radius is stated on the figure.

## Slide 8
The deformable mirrors are real
A 20 nm actuator poke lands where it is put, at twice the surface
• The model. Two 32×32-actuator DMs as grid-data surfaces in their own frames, 880 actuators each inside the 47 mm beam, influence functions with nearest-neighbour coupling.
• The gate. One actuator poked 20 nm, half a pupil radius off centre: the exit-pupil wavefront answers with 3.92e-08 m peak against 4e-08 expected (twice the surface, for a mirror), 100% of the response energy within 0.15 pupil radii of the peak, peak at 0.53 radii off centre.
• Why it is a gate. The failure mode of a wrongly-framed grid surface is a response painted at the pupil centre — localisation is the proof the actuator geometry is right.
The single-actuator response at the exit pupil: localised, off-centre, 2× the commanded surface.

## Slide 9
What the segment gaps cost
1298× in dark-zone contrast, same mask on both apertures
• The measurement. The same apodized-pupil Lyot coronagraph on the segmented primary and on a monolithic twin of the identical telescope.
• Segmented: 4.705e-07 mean contrast, 6.18e+03 on-axis suppression.
• Monolithic: 3.624e-10 mean, 2.82e+07 suppression.
• The ratio is the gaps and nothing else — 1298× in the mean, 3809× in the median; both trains share the same wavefront.
• These are open-loop numbers: the DMs are flat here. The loop slide prices what they buy.
Radial contrast, both apertures, dark zone shaded. The segmented curve plateaus where the monolithic one keeps falling — that plateau is gap-scattered light.

## Slide 10
Six coronagraphs, one train
Pre-control: the apodized Lyot leads at 4.4e-07; the vortex pays the gaps ~40x
• The design rule that made them comparable. On a segmented hex aperture the coronagraph's pupil is a CIRCULAR STOP at the apodizer plane — the telescope's hex envelope is upstream optics, not the coronagraph pupil. Every family below sees the same circularized, gapped pupil; contrast normalizes to its bare peak, and the stop's ~8% collecting-area cost sits in the throughput column.
• The families (dark-zone mean, PRE-CONTROL | throughput): classical Lyot 3.50e-06 pre-control, 23% throughput; apodized Lyot 4.37e-07 pre-control, 9% throughput; APLC 2.18e-06 pre-control, 8% throughput (aperture-matched prolate: solver-limited, flag stands); band-limited 1.64e-06 pre-control, 12% throughput; vortex c4 1.64e-05 pre-control, 33% throughput; c6 1.87e-05 pre-control, 33% throughput — the vortex passes the segment-gap light the occulting families block.
• The stop's 2.16x on the bare occulter, attributed by measurement: entirely the stop edge at fixed masks (the scale re-reference contributes 1.00x); the Babinet split shows the edge enters by coherent INTERFERENCE with the gap field (cross 6.5e-06 vs the rim's own 2.5e-06) — coherent, hence in the loop's reach. The next slide cashes that.
The six families, statics on the circularized segmented train.

## Slide 11
The loop on every family
All six floors sit within 2x of their own Jacobian's linear-achievable: the substrate speaks, not the controller
• static -> relin floor | linear-achievable at the achieved stroke: classical Lyot 3.5e-06 -> 3.9e-07 | 2.1e-07; apodized Lyot 4.5e-07 -> 1.1e-07 | 1.1e-07 (the campaign floor); APLC 1.1e-06 -> 7.5e-07 | 7.5e-07; band-limited 1.6e-06 -> 1.3e-06 | 7.2e-07; vortex c4 1.6e-05 -> 5.4e-06 | 5.5e-06; c6 1.8e-05 -> 3.9e-06 | 4.7e-06.
• The stopped occulter digs 8.9x where its no-stop self dug 5.2x — the loop claws back most of the coherent edge term the previous slide measured.
• The vortices are linear-optimal: relinearization pays 2.5-3.7x where the fixed Jacobian paid 1.2x (gap-chasing strokes reach the linearity boundary early), and the residual gap leak is uncontrollable at this amplitude authority.
• The knob is the DM spacing: z/z_T = 3.7e-03 at the outer working angle — Talbot-weak amplitude authority is the common ceiling; the spacing trade prices it.
Convergence per family (relinearization joins at the dotted lines) and the closed-loop column.

## Slide 12
The Lyot trade
Throughput is bought with contrast on every leg; the operating points were chosen, not defaulted
• The sweep. Lyot fraction against contrast AND throughput for the vortex legs and the apodized-Lyot leg, statics under the stop; stars mark the S1 operating points the campaign scored.
Contrast vs Lyot fraction (left) and the contrast-throughput trade with the family operating points (right).

## Slide 13
The error budget closes
Engine vs model: worst 0.35% over a segment, a DM and a relay mirror, all six freedoms
• The model. Wavefront sensitivity to every rigid-body freedom of 31 optics — the segments, the fold mirrors, the relay and both DMs — plus segment figure modes and a per-segment influence basis: 192 + 152 + 114 channels over five field points.
• The closure check. Poke a segment, a DM and a relay mirror through the engine and compare with the model, at the surface the model was harvested at: worst relative error 0.0035 over 18 freedom pairs. The matching check in the previous build disagreed by factors up to 55; the resolution is in the backup, and it was not the model.
• The assembly exhibit. The 19 segments perturbed as one body against one segment alone: tilt adds up (ratio 16.9), piston cancels (ratio 0.028), clocking is invisible per segment and real for the assembly.
freedom | assembly response | assembly / one segment
Rx | 2.619 | 16.88
Ry | 2.506 | 16.12
Rz | 0.2475 | 9.324e+04
Tx | 0.06566 | 16.2
Ty | 0.06706 | 16.6
Tz | 0.0136 | 0.0282
Column RMS of wavefront change per unit motion; rotations per radian, translations per metre.
Singular values of the three Jacobians, largest normalised to one.

## Slide 14
The metrology truss
114 laser gauges + 252 edge sensors, validated against the engine to 0%
• The layout. Six launchers per segment on its true boundary, fiducials on the secondary's rim, plus inter-segment edge sensors — the committed metrology stage run on this telescope with this train's sensitivity model.
• What it buys. Post-control wavefront residual 0.86 nm per nm of gauge noise with edges and gauges together, against 0 for gauges alone — the edge sensors carry the segment-to-segment state.
• Validated. The layout merit's finite-difference check closes at 0%, and a 200-draw Monte-Carlo estimate/control loop lands within 2.6% of the analytic residual.
The as-built truss: beams from the 19 segments to the hub fiducials; edge sensors on the segment boundaries.

## Slide 15
The loop closes
The dark zone held under drift: 2.5e-07 against 1.7e-06 open-loop
• The drift. 41 frames over 7 minutes: random walk plus correlated drift on every freedom of all 19 segments, played through the engine on the full train.
• The rigid-body loop. Edge and gauge readings, a weighted least-squares estimate, an integrating controller on all six freedoms of every segment: the state residual holds at 0.36 nm while the open-loop drift grows to 2.9 nm.
• The DM loop. The measured actuator Jacobian digs the dark zone 4.6e-07 → 1.9e-07, then a damped re-solve at each scored frame holds it: 1.91e-07 → 2.46e-07 closed, against 4.65e-07 → 1.72e-06 open.
• The honest line. Closed-loop pupil wavefront is larger than uncorrected — that is the DM stroke the contrast is bought with, and the figure labels it as such.
State, wavefront and contrast against time. The contrast panel is the payoff: open loop degrades 3.7×; the closed loop holds.

## Slide 16
What this demonstrates
One model, from surface figure to a held dark zone
• A design becomes an instrument becomes an error budget becomes a controlled observatory, without leaving the model or re-entering the geometry anywhere.
• The gap penalty is measured, not assumed — 1298× open loop — and the control loop that answers it is measured too: 1.7e-06 open against 2.5e-07 closed at the end of the soak.
• Every model-vs-engine comparison closes — worst 0.0035 across segments, DMs and relay optics — because the comparison is made at the surface the model lives on. Where a build disagreed, the deck says why and what fixed it.
• All of it is committed: prescriptions, runners, reports, and this deck's numbers are one git clone away.

## Slide 17
Backup Slides

## Slide 18
The stop's edge, measured
A Babinet split with 1e-15 closure: the edge interferes, it does not merely add
• Method. The circular stop applied as a SCREEN on the no-stop chain holds every mask and scale fixed, so E_rim = E_hex - E_screened is exactly the blocked rim's field. Pins: screened bare peak == stopped bare peak to 0.0e0; both S1 records reproduced under 1%.
• The split (dark-zone mean energy): I_ns 1.09e-05 + rim 2.53e-06 + cross 6.54e-06 — the rim's own ring is ~28% of the increase; the cross term (coherent interference with the pre-existing gap speckle) is 2.6x larger. Peak renormalization 1.178x; dark-zone energy up 1.83x at fixed masks; the lambda/D re-reference contributes 1.00x.
• The APLC flag, restated: the stopped aperture-matched prolate hit its iteration cap unconverged (the answer moves with the cap — not an eigenfunction, not a design); its row stands flagged, and the block/Lanczos eigensolver or the N'Diaye LP co-design are the named, deferred machines.
Where the stop's edge lands: no-stop, stop-as-screen, and the rim field alone.

## Slide 19
The round-1 disagreement, resolved
The same basis includes the evaluation surface
• The symptom. Engine and linear model disagreed by 1–55× on every segment freedom but piston, which agreed to 0.6%.
• The cause, measured. The check traced to the Science focal plane; the model lives at the coronagraph exit pupil. At a focal plane a segment tilt is a footprint piston with lever = the segment's pupil radius — at that segment, 6.5× the tilt response, which is exactly the "mystery factor" the fingerprint carried. Piston agreed because a normal displacement adds path uniformly at any surface.
• Same element, same pokes, one changed trace target — the table.
• The fix is structural. The closure check is now a shared function that takes the evaluation surface from the harvest artifact, with a regression test that fails if a rotation ever closes at the wrong surface.
freedom | rel. error at the focal plane | at the model's surface
Rx | 56.9 | 3.34e-05
Ry | 1.01 | 3.48e-05
Rz | 1.04 | NaN
Tx | 1.01 | 0.00131
Ty | 54.8 | 0.00131
Tz | 0.00614 | 1.06e-05
Segment 19, 1 nm / 1 nrad pokes against the stored sensitivity columns. "NaN" rows are the segment-clocking null (response below the 1 pm floor).

## Slide 20
Choosing a stable control law
Two mechanizations rejected by measurement
• A held one-shot correction (the round-1 idiom, with real sensor noise): at the solve frame the drift sits below the 1 nm edge noise, the estimate residual exceeds the state, and the corrected leg ends worse than the uncorrected one.
• A per-frame loop on the estimator's segment slice: the full-body minimum-variance gain is contractive, its segment slice is not (spectral radius 1.154) — the engine loop diverged to 19 nm on a 3 nm drift, and a pure-linear simulation predicts the divergence to three digits.
• Shipped: weighted least squares with ridge on the segment state (radius 0.9998, gain 0.5): converges to the 0.36 nm sensor-noise floor.
• The DM re-solve needed the same care. Undamped solves against gap speckle — amplitude-dominated, weakly controllable at this DM spacing — push stroke along near-null directions and diverge; damping (0.7) plus a small leak (0.02) makes the dig monotone and held. DM spacing as an amplitude-authority knob is a stated design trade, not exercised here.

## Slide 21
Packaging the longer relay
Fold side is a stability choice, not a taste choice
• A near-normal fold turns the chief by 180° − 2·AOI, and the beam direction reverses at each mirror.
• Alternating the fold side — fine for the five folds of the shorter round-1 relay — adds −2·AOI of net rotation per fold: over this chain's ten folds the accordion fans ~120° and walks to a 10.33 m shroud diameter. Measured, with the element positions in the record.
• Keeping the same side every fold ping-pongs the beam between two fixed directions and packs the chain into a leg-sized pocket: 7.451 m, identical to the primary-set envelope. The DM-bearing back end costs nothing in shroud diameter.

## Slide 22
Focal ratio: why f/25.4 and not f/12–20
The corrected focal ratio is not a continuous function of the layout
• The surface-figure solve spends optical power, so the focal ratio must be read on the corrected system; a search on the tertiary radius lands in different solve basins and refuses to steer continuously (f/15.5 and f/25.7 at layouts 0.36% apart).
• The design point was chosen on wavefront, which it meets; the slower focal ratio also puts more λ/D on the focal-plane mask, easing its fabrication.

## Slide 23
What an apodizer alone does not buy back
The round-1 negative result stands
• Redesigning the apodizer for the segmented pupil — a linear-program optimum and an aperture-specific eigenfunction — recovered essentially nothing: the gaps scatter light no transmission profile removes.
• The optimizer's design model (a single Fourier transform) floors five times above what the engine already reaches, and the disagreement grows the harder the optimizer is pushed — the signature of an optimizer mining its model, worth reusing as a diagnostic anywhere a design model is cheaper than the simulator it feeds.
• The round-2 answer is the deformable mirrors: measured against the engine, they dig the segmented floor 4.6e-07 → 1.9e-07 and hold it under drift.

## Slide 24
What is not in this model
Stated, not omitted
• The coronagraph masks are clear-pupil designs. Co-optimising apodizer, occulter and Lyot for the segmented aperture is known, separate work; the open-loop 1298× is the size of that prize.
• Monochromatic, at 500 nm. The bandwidth and polarization layers exist on the testbed substrate and are configuration away, not new machinery.
• The metrology measurement is simulated from its validated linear model plus noise, not a second engine trace of the truss; the engine holds the truss points rigid, so the model is the only figure source either way.
• DM spacing (47 mm pupil, 0.15 m apart) limits amplitude-speckle authority; the testbed's wider spacing is the knob, and re-running the chain at another spacing is parameter work.

## Slide 25
How to reproduce
Every number on these slides comes from these runs
• Round 1 (frozen): s1_layout_search, s1_telescope, s2_segmentation — the telescope and the segmented primary.
• r1_backend, r1_coro, r1_dm, r1_shroud_union — the DM-bearing train, the coronagraph on both apertures, the DM surfaces, the two-leg shroud.
• r2_sequence_fig, r2_bench_fig, r2_masks_fig — the four exhibit graphics.
• r3_sensitivities, r3_dm_jacobian, r3_met — the error budget, the actuator Jacobian, the metrology stage.
• r4_timeseries — the closed-loop drift series.
• python3 deck_e2e6m_r2.py — this deck, from the reports those runs wrote.
All knobs live in one parameter file. The narrative record — every question, decision and gate — is the campaign log beside the runners.